Evaluation of gvSIG and SEXTANTE Tools for Hydrological Analysis
6th gvSIG Conference, Valencia, SPAIN
Prof. Dr-Ing Dietrich Schrödera
Mudogah Hildahb and Franz Davidb
Stuttgart University of Applied Sciences
        dietrich.schroeder@hft-stuttgart.de

---
Introduction
Image taken from:
http://www.statemaster.com/encyclopedia/Black-Forest
Image taken from:
http://upload.wikimedia.org/wikipedia/commons/
thumb/a/a0/G%C3%BCtenbach_in_VS.svg/300px-G%C3%BCtenbach_in_VS.svg.png
Image taken from:
http://www.the-english-guest-house.com/thedanube.htm

---
Data
ESRI Shapefiles
- Climate Stations
- Rivers
- Landcover
DEM (ASCII )
Topographic maps (TIF) - 1:25,000
Rainfall Data (mm/m2)

---
Methodology
Methodology
Methodology
Interpolation of rainfall data
Stream network extraction
Watershed delineation
Surface run-off calculation
General Analysis
Breg and Brigach
Hydrological
 Analysis
Watershed delineation
Flow Velocity Map
Flow Length / Time
Detailed Analysis
Linach Creek
Dam Analyses
Volume calculation
Viewshed Analysis

---
Breg and Brigach
Breg and Brigach
Coarse, simplified hydrological modelling of greater region (40 x 55 km2)
Interpolation of the rainfall data
  - IDW, Nearest Neighbour and Kriging
Stream network extraction
  - ‘Burn-in’ approach
- Watershed delineation
- Surface run-off calculation

---
Interpolation of Rainfall
Interpolation of Rainfall
Nearest Neighbour
IDW
- IDW
- Nearest Neighbour
- Spatial Autocorrelation
- Kriging
Kriging
[Speaker Notes: Climate Table in Excel converted to DBF format and joined to the climate location shapefile. Interpolation done based on the annual rainfall field. Several methods tried: IDW – bulls-eye effect, Nearest neighbour, Kriging.]

---
‘Burn-in’
- Rivers rasterized by defined value
- DEM reduced by rasterized rivers
  !! Reclassify
- Buffer
- Rasterize Vector Layer
- Raster Difference (-)
Reduced DEM

---
Watershed Delineation
Watershed Delineation
Sink
Filling
Flow
Accumulation
Channel Network
Watershed
Generic error with Flow accumulation tool
Workaround using r.watershed tool in GRASS
Extracting only the Breg and Brigach rivers
Adopt results from external system

---
Surface Runoff
Surface Runoff
- Infiltration and evapo - transpiration are homogenous
- 75% of annual rainfall participates in the runoff
- Raster Calculator
- Basic Statistics
- Invariable annual average temperature
- Uniform vegetation of conifer forest and pasture land
- The soil type doesn’t change
Result: 414,975m3
Ref System: 410,835m3

---
Linach Creek
Interpolation of rainfall data
Stream network extraction
Watershed delineation
Surface run-off calculation
General Analysis
Breg and Brigach
Hydrological
 Analysis
Watershed delineation
Flow Velocity Map
Flow Length / Time
Detailed Analysis
Linach Creek
Dam Analyses
Volume calculation
Viewshed Analysis

---
DEM Creation
DEM Creation
- Rasterize contour lines
- Random Bernoulli of
  (0 and 1)
- Product of the two rasters to get random distribution of point information
- Remove NODATA values
- Interpolation using IDW with 5m interval
- Rasterize Layer
- Random Bernoulli
- Raster Product (*)

---
Hydrological Analysis
Watershed Delineation
Sink Filling
Flow Accumulation
Watershed Tool
Merged watershed with channel network
- Raster to Vector
- GeoProcessing Toolbox
- Dissolve

---
Flow Maps
Flow Maps
- Slope Length
- Slope
- Raster Calculator
Hydrological Length Map
Slope
Resistance Layer
Velocity calculated using Manning Strickler Eq.
Velocity Map
V = Kst * R2/3 * S1/2
Kst=Resistance Layer
R = Hydraulic Radius
S= Slope raster

---
Flow time Map & Time-area Diagram
Flow Time Map & Time-area Diagram
Time Map created using DEM and Channel Network
Reclassification flow time map into constant time	intervals
Derive area for each time interval
Time-area diagram calculation
Hydrograph
- Time to Outlet
- Reclassify
- Class Statistics
- Geomorphological Instantaneous Unit Hydrograph

---
Volume Calculations
Volume Calculations
Free-board Layer of 845 m
DEM for DAM
Volume Between Two layers
gvSIG: 1,655,929,566 m3
Ref: 1,655,925,131m3
- Constant Grid
- Volume Between Two Layers

---
Viewshed Analysis
Viewshed Analysis
To establish the location of control points for surveying the dam
  - Conifers from Landcover used as an obstacle layer of 10m
  - Visibility radius was set to 3km
- Rasterize Vector Layer
- Raster Addition (+)
- Visibility Tool
Tool only supports one observer position

---
Challenges
Challenges
- Problems with interpretation of NODATA values
- NODATA values (often assigned -99,999) used in calculations therefore giving erroneous results
- Some tools are too time-consuming
- Some tools have an implied size limitation; they don’t run on large datasets but work well on smaller ones
- Bugs still exist in some tools

---
Conclusion
Conclusion
- gvSIG and SEXTANTE (with GRASS) interface are together very powerful tools
- Duplicate tools (GRASS and SEXTANTE) make up for each other
- In general:
  - 80% of tools worked well
  - 20% (Error report or Wrong output)
Recommendations
  - Extend tool documentation (parameter clues, units etc)
  - Non modal mode for windows would enhance interaction between the tool and map interfaces

---
Thank You